## Slide 1: LLMs and Robotics
TEACHING ROBOTS AND NAVIGATION
From embodied agency to vision-language-action models, robot-use agents and world models

## Slide 2: Will an embodied LLM have agency?
If we embody LLMs in a robot, will they have agency?
Alter3, a humanoid driven by an LLM: does it show a sense of agency?
Can Alter3 recognize itself when looking in a mirror?
Reading: Ikegami et al., Minimal Self in Humanoid Robot Alter3 Driven by a Large Language Model (arXiv 2406.11420)
LLMs and Robotics
2

## Slide 3: Inside a VLA model
State tokens: internal state and sensor data (e.g. LIDAR)
Action tokens: generated autoregressively, each one a low-level control signal such as a joint angle update or torque
Memory carries context across a long task, such as drying the counter with a sponge
LLMs and Robotics
3

## Slide 4: VLMs versus VLAs
VLM (GPT-4o, Gemini, SayCan): image plus text in, text, plans or code out; needs downstream controllers
VLA (OpenVLA, Octo, π0): camera frames plus text in, continuous 7-DoF deltas out (x, y, z, roll, pitch, yaw, gripper)
One network unifies perception, instruction understanding and control
LLMs and Robotics
4

## Slide 5: Safety of VLA models
Visual input and language go straight to motor commands
Open-world use needs robust behavioral safety guards
Current VLAs lack them: adversarial images, jailbreaks and unsafe commands
Discuss: what are the safety implications?
LLMs and Robotics
5

## Slide 6: The era of robot-use agents
General-purpose models that control different robots, write policies and learn new physical tasks with little robot-specific training.
Philip Isola, MIT
Bitter Lesson (Sutton): leverage data and the LLM ability to write code and transfer it across domains.
LLMs and Robotics
6

## Slide 7: LLM puppeteering from the cloud
A shift from bespoke hardware to LLM agents with hardware in the loop
Intelligence runs in the cloud and is not tuned to one robot
A non-intelligent device could become AI-enabled with a software update
Caution: puppeteering may be less reliable than proven robotic systems in safety-critical use
LLMs and Robotics
7

## Slide 8: Claude plays robotics: 11 locomotion tasks
Task | What it tests
find_x | Walk to a table marked with a blue X, 25 ft away
visual_search | Find a red sphere hidden behind occluders in a 12 × 12 m arena
color_sequence | Visit colored circles in order; working memory
return_home | Follow waypoints, then return to origin from memory
procedural_maze | Navigate a maze with the forward camera only
invisible_walls | Replan around walls that cannot be seen
obstacle_course | Pass gaps; know the robot’s dimensions
oneshot_course | Plan the whole command sequence from a top-down map
drift_detection | Notice silently corrupted commands and compensate
turn_correction | See that a turn was incomplete and correct it
explore_report | Explore, then answer layout questions from memory
LLMs and Robotics
8

## Slide 9: World models and spatial reasoning
Discuss: will LLMs struggle with spatial reasoning?
Fei-Fei Li: a fully consistent 3D world is required for navigation
LeCun: robots need AI that anticipates the consequences of actions
Text-only intelligence lacks the physical grounding; a world model lets an agent test plans safely in simulation
LLMs and Robotics
9

## Slide 10: Bottlenecks for robotics (c. 2026)
LLMs and Robotics
10

## Slide 11: What about explainability?
Is explainability important for these robots? Discuss.
It links to competence versus performance
LLMs may hallucinate their explanations
LLMs and Robotics
11

## Slide 12: Summary: embodied AI models and challenges
LLMs and Robotics
12

## Slide 13: Practicals, benchmarks and roadmap
Script A: a conceptual VLA in PyTorch, CPU only
Script B: OpenVLA-7B with 4-bit quantization on a Colab T4
Benchmarks: LIBERO, DROID, RoboCasa, BEHAVIOR-1K
Tools: LeRobot, Open X-Embodiment, inspect-robots
Vision → Language → Action → Data → Training → Evaluation → Deployment
LLMs and Robotics
13